## Slide 1
-S
IMPLEMENTATION OF VERILOG PROGRAMMING IN AD9910 HARDWARE BY AUTO CODE GENERATION Adrija Ghosh Defence Institute of Advanced Technology (Electronics Dept., R&C) Guides: Dr. M. Veerendra (Sc. E, RCI, DRDO) Dr. Kailas Sawant (DIAT) |  |  | 
PROPOSED METHODOLOGY |  |  | 
INTRODUCTION The aim of this project is to automate the code generation of Verilog code for the AD9910 using Simulink, so that Simulink models can be utilized to generate radar waveforms used in real- life radar applications. PROBLEM STATEMENT To auto-generate and deploy Verilog code on AD9910 hardware for the realization of a complete Hardware-in-the- Loop (HIL) architecture. OBJECTIVES To design and integrate HDL-compatible Simulink models for polyphase (P1–P4) and LFM waveform generation. To auto-generate Verilog code from Simulink for configuring the AD9910 DDS hardware. To establish an HIL setup by interfacing the FPGA/DSP board with the AD9910 DDS and ADC via SPI. To implement and validate the RF transmit– receive chain for polyphase and LFM waveforms using oscilloscope and receiver modules. To digitize the received signals and feed them back to the FPGA/DSP board for evaluation and usage. | FUNCTIONAL DIAGRAM |  | 
 |  | SYSTEM IMPLEMENTATION HDL-compatible Simulink models for generating polyphase (P1–P4) and LFM waveforms are designed. Verilog code is generated by auto-code generation from the Simulink model and used to configure the AD9910 DDS hardware. A Hardware-in-the-Loop (HIL) setup is established by interfacing the FPGA/DSP board with the AD9910 DDS and ADC modules via SPI. The generated waveforms are transmitted through the RF transmit–receive chain and validated using an oscilloscope and a receiver module. The received signals are digitized using the ADC and fed back to the FPGA for evaluation. | 
PRACTICAL APPLICATIONS OF FUTURE SCOPE REFERENCES MODEL 1. Abdullah, Hikmat N., and Hussein A. Hadi. "Design and Implemetation of FPGA based Software Defined Radio The system can be improved by allowing waveform Using Simulink HDL Coder." (2009). 2. AD9910 Datasheet, Radar waveform generation for pulse compression and parameters such as frequency and phase to be changed https://www.analog.com/media/en/tec hnical-documentation/data- target detection applications. during operation. sheets/ad9910.pdf 3. Chen, Dongdong, Xinhui Cui, Qidong Zhang, Di Li, Wenyang Cheng, Chunlong Real-time validation of DDS-based signal generation • This will help in testing different signal conditions Fei, and Yintang Yang. "A survey on analog-to-digital converter integrated by Hardware-in-the-Loop (HIL) testing. without redesigning the hardware and improve the re- circuits for miniaturized high resolution ultrasonic imaging system." Rapid prototyping and verification of FPGA-based usability of the system. Micromachines 13, no. 1 (2022): 114. 4. Corelis, Inc.. BusPro High-Speed waveform generators for defence RF systems. • Additional analysis tools may be added to automatically Multi-IO SPI Host, Debugger, and Programmer User’s Manual, Edition 3. Testing of radar waveforms with reduced time and check incoming waveform quality, which may reduce November 2021. 5. da Silva, Alexandre César Rodrigues. resource usage through auto-generated hardware code. manual measurements using instruments, save time, and "Code Generation From MATLAB– Simulink Models." MATLAB: improve testing efficiency. Applications for the Practical Engineer (2014): 419. |  |  |